## Slide 1: 3D Vision
Topic 2 of Part II
Calibration
Computer Vision
Zhigang Zhu, City College of New York zzhu@ccny.cuny.edu
Notes: This course is a basic introduction to parts of the field of computer vision. This version of the course covers topics in 'early' or 'low' level vision and parts of 'intermediate' level vision. It assumes no background in computer vision, a minimal background in Artificial Intelligence and only basic concepts in calculus, linear algebra, and probability theory.

## Slide 2: Lecture Outline
Calibration: Find the intrinsic and extrinsic parameters
  Problem and assumptions
  Direct parameter estimation approach
  Projection matrix approach
Direct Parameter Estimation Approach
  Basic equations (from Camera Model Lecture)
  Homogeneous System
  Estimating the Image center using vanishing points
  SVD (Singular Value Decomposition)
  Focal length, Aspect ratio, and extrinsic parameters
  Discussion: Why not do all the parameters together?
Projection Matrix Approach (…after-class reading)
  Estimating the projection matrix M
  Computing the camera parameters from M
  Discussion
Comparison and Summary
  Any difference?

## Slide 3: Camera Model
Coordinate Systems
  Frame coordinates (xim, yim) pixels
  Image coordinates (x,y) in mm
  Camera coordinates (X,Y,Z)
  World coordinates (Xw,Yw,Zw)
Camera Parameters
  Intrinsic Parameters (of the camera and the frame grabber): link the frame coordinates of an image point with its corresponding camera coordinates
  Extrinsic parameters: define the location and orientation of the camera coordinate system with respect to the world coordinate system
Zw
Xw
Yw
Y
X
Z
x
y
O
Pw
P
p
xim
yim
(xim,yim)
Pose / Camera
Object / World
Image frame
Frame Grabber
Notes: The entire story of the camera model: from world to camera (coordinate systems), and from camera (3D) to image frame (2D).
The intrinsic parameters should be listed in the specifications of the camera and the frame grabber by the manufacturers, but not really….
The extrinsic parameters describe the pose (position and orientation) of the camera looking at the scene.

## Slide 4: Problem and Assumptions
Given one or more images of a calibration pattern,
Estimate
  The intrinsic parameters
  The extrinsic parameters, or
  BOTH
Issues: Accuracy of Calibration
  How to design and measure the calibration pattern
    Distribution of the control points to assure stability of solution – not coplanar
    Construction tolerance one or two order of magnitude smaller than the desired accuracy of calibration
    e.g. 0.01 mm tolerance versus 0.1mm desired accuracy
  How to extract the image correspondences
    Corner detection?
    Line fitting?
  Algorithms for camera calibration given both 3D-2D pairs
Alternative approach: 3D from un-calibrated camera
Notes: Our goal is to build the geometric relations between a 3D scene and its 2D images for both computer vision and computer graphics. The relations include two aspects: 3D transformation that represents the viewpoints and viewing directions of the camera (real or virtual), and the perspective projection maps 3D points into 2D images.
Note that we can use the same sets of equations for both vision and graphics. However vision is much harder than graphics: In graphics, 2D projections can be easily generated from 3D models, given the 3D models and the (virtual) camera parameters. In computer vision, the projections are fulfilled by a real camera. We want to reconstruct the 3D models from the 2D images. The inverse problems are much harder since (1) we need to find out the intrinsic and extrinsic camera parameters by the so called calibration procedure; and (2) we need to recover 3D from 2D images in which the third dimension is lost.

## Slide 5: Linear Version of Perspective Projection
World to Camera
  Camera: P = (X,Y,Z)T
  World: Pw = (Xw,Yw,Zw)T
  Transform: R, T
Camera to Image
  Camera: P = (X,Y,Z)T
  Image: p = (x,y)T
  Not linear equations
Image to Frame
  Neglecting distortion
  Frame (xim, yim)T
World to Frame
  (Xw,Yw,Zw)T -> (xim, yim)T
  Effective focal lengths
    fx = f/sx, fy=f/sy
Notes: The 4th equation is derived from the three basic equations (pose, projection and frame), which directly maps a 3D world point to its frame coordinates

## Slide 6: Direct Parameter Method
Extrinsic Parameters
  R, 3x3 rotation matrix
    Three angles a,b,g
  T, 3-D translation vector
Intrinsic Parameters
  fx, fy :effective focal length in pixel
    a = fx/fy = sy/sx, and fx
  (ox, oy): known Image center -> (x’,y’) known
  k1, radial distortion coefficient: neglect it in the basic algorithm
Same Denominator in the two Equations
  Known : (Xw,Yw,Zw) and its (x’,y’)
  Unknown: rpq, Tx, Ty, fx, fy
Notes: A BIG question: Here we assume that the coordinates of the image center are known. Can we assume (in other words) that the image center is the origin of the frame coordinate system as suggested in the textbook (p. 127)?
The answer is NO. Since we cannot eliminate (Ox,Oy) from the linearized equation;

## Slide 7: Linear Equations
Linear Equation of 8 unknowns v = (v1,…,v8)
  Aspect ratio: a = fx/fy
  Point pairs , {(Xi, Yi,, Zi) <-> (xi, yi) } drop the ‘ and subscript “w”
Notes: How to construct a system of linear equations

## Slide 8: Homogeneous System
Homogeneous System of N Linear Equations
  Given N corresponding pairs {(Xi, Yi,, Zi) <-> (xi, yi) }, i=1,2,…N
  8 unknowns v = (v1,…,v8)T, 7 independent parameters
The system has a nontrivial solution (up to a scale)
  IF N >= 7 and N points are not coplanar => Rank (A) = 7
  Can be determined from the SVD of A
Notes: Show what are the solutions in the blackboard
Trivial solution V= 0. It is not the correct solution since R cannot be all zeros
V0 is a solution of the homogeneous system -> SO is k V0 (k any number including 0)

## Slide 9: SVD: definition
Singular Value Decomposition:
  Any mxn matrix can be written as the product of three matrices
Singular values si are fully determined by A
  D is diagonal: dij =0 if ij; dii = si (i=1,2,…,n)
  s1  s2  … sN  0
Both U and V are not unique
  Columns of each are mutual orthogonal vectors
V1
U1
Appendix A.6
Notes: Notice the Transpose in V; simply want to say columns of both U and V are eigen vectors of ….

## Slide 10: SVD: properties
1. Singularity and Condition Number
  nxn A is nonsingular IFF all singular values are nonzero
  Condition number : degree of singularity of A
    A is ill-conditioned if 1/C is comparable to the arithmetic precision of your machine; almost singular
2. Rank of a square matrix A
  Rank (A) = number of nonzero singular values
3. Inverse of a square Matrix
  If A is nonsingular
  In general, the pseudo-inverse of A
4. Eigenvalues and Eigenvectors (questions)
  Eigenvalues of both ATA and AAT are si2 (si > 0)
  The columns of U are the eigenvectors of AAT (mxm)
  The columns of V are the eigenvectors of ATA (nxn)
Notes: Property 1 :
can be used to examine how robust the linear equation system
Property 3:
Prove A-1 A = I
What is D–1 ? simply d-1ij = 1/dij
What is D0-1 ? Equal to D– for all nonzero singular values and zero otherwise
Property 4:
Prove them in homework

## Slide 11: SVD: Application 1
Least Square
  Solve a system of m equations for n unknowns x(m >= n)
  A is a mxn matrix of the coefficients
  b (0) is the m-D vector of the data
  Solution:
  How to solve: compute the pseudo-inverse of ATA by SVD
    (ATA)+ is more likely to coincide with (ATA)-1 given m > n
    Always a good idea to look at the condition number of ATA
nxn matrix
Pseudo-inverse
Notes: Can be nicely applied where least square method is used

## Slide 12: SVD: Application 2
Homogeneous System
  m equations for n unknowns x(m >= n-1)
  Rank (A) = n-1 (by looking at the SVD of A)
  A non-trivial solution (up to a arbitrary scale) by SVD:
  Simply proportional to the eigenvector corresponding to the only zero eigenvalue of ATA (nxn matrix)
Note:
  All the other eigenvalues are positive because Rank (A)=n-1
  Try to prove it.
  In practice, the eigenvector (i.e. vn) corresponding to the minimum eigenvalue of ATA, i.e. sn2
Notes: Will be used in solving the 7 unknown equations for calibration

## Slide 13: SVD: Application 3
Problem Statements
  Numerical estimate of a matrix A whose entries are not independent
  Errors introduced by noise alter the estimate to Â
Enforcing Constraints by SVD
  Take orthogonal matrix A as an example
  Find the closest matrix to Â, which satisfies the constraints exactly
    SVD of Â
    Observation: D = I (all the singular values are 1) if A is orthogonal
    Solution: changing the singular values to those expected
Notes: Will be used in the rotation matrix estimation

## Slide 14: Homogeneous System
Homogeneous System of N Linear Equations
  Given N corresponding pairs {(Xi, Yi,, Zi) <-> (xi, yi) }, i=1,2,…N
  8 unknowns v = (v1,…,v8)T, 7 independent parameters
The system has a nontrivial solution (up to a scale)
  IF N >= 7 and N points are not coplanar => Rank (A) = 7
  Can be determined from the SVD of A
  Rows of VT: eigenvectors {ei} of ATA
  Solution: the 8th row e8 corresponding to the only zero singular value l8=0
Practical Consideration
  The errors in localizing image and world points may make the rank of A to be maximum (8)
  In this case select the eigenvector corresponding to the smallest eigenvalue.
Notes: Trivial solution V= 0. It is not the correct solution since R cannot be all zeros
V0 is a solution of the homogeneous system -> SO does k V0 (k any number includes 0)

## Slide 15: Scale Factor and Aspect Ratio
Equations for scale factor g and aspect ratio a
Knowledge: R is an orthogonal matrix
Second row (i=j=2):
First row (i=j=1)
v1 v2 v3 v4 v5 v6 v7 v8
Notes: the length (magnitude) of vector Ri is 1

## Slide 16: Rotation R and Translation T
Equations for first 2 rows of R and T given a and |g|
First 2 rows of R and T can be found up to a common sign s (+ or -)
The third row of the rotation matrix by vector product
Remaining Questions :
  How to find the sign s?
  Is R orthogonal?
  How to find Tz and fx, fy?

## Slide 17: Find the sign s
Facts:
  fx > 0
  Zc >0
  x known
  Xw,Yw,Zw known
Solution
  Check the sign of Xc
  Should be opposite to x
Zw
Xw
Yw
Y
X
Z
x
y
O
Pw
P
p
xim
yim
(xim,yim)

## Slide 18: Rotation R : Orthogonality
Question:
  First 2 rows of R are calculated without using the mutual orthogonal constraint
Solution:
  Use SVD of estimate R
Replace the diagonal matrix D with the 3x3 identity matrix
Notes: The second time SVD is used

## Slide 19: Find Tz, Fx and Fy
Solution
  Solve the system of N linear equations with two unknown
    Tx, fx
  Least Square method
  SVD method to find inverse
ai2
ai1
bi
Notes: The third time SVD is used
a = fx / fy => fy = fx / a

## Slide 20: Direct parameter Calibration Summary
Algorithm
  Measure N 3D coordinates (Xi, Yi,Zi)
  Locate their corresponding image points (xi,yi) - Edge, Corner, Hough
  Build matrix A of a homogeneous system Av = 0
  Compute SVD of A , solution v
  Determine aspect ratio a and scale |g|
  Recover the first two rows of R and the first two components of T up to a sign
  Determine sign s of g by checking the projection equation
  Compute the 3rd row of R by vector product, and enforce orthogonality constraint by SVD
  Solve Tz and fx using Least Square and SVD, then fy = fx / a
Yw
Xw
Zw
Notes: Two important steps:
Build a linear system
Decompose intrinsic and extrinsic parameters using physical constraints of the camera (orthogonality of R, sign of depth, ….)
SVD is used three times
homogeneous system
enforcing orthogonality constraints
solve least square system

## Slide 21: Discussions
Questions
  Can we select an arbitrary image center for solving other parameters?
  How to find the image center (ox,oy)?
  How about to include the radial distortion?
  Why not solve all the parameters once ?
    How many unknown with ox, oy? --- 20 ??? – projection matrix method
Notes: Direct parameter method: One point pair will provide 1 linear equation of 8 unknowns (7 independent)
Projection matrix method: One point pair will provide 2 linear equations of 12 = (4+4+4) unknowns (11 independent)
All in one method (including image center): One point pair will provide 2 equations of 14 (4+4+4+2) unknowns, 2 linear equations of 20 (4+4+4+4+4) unknowns

## Slide 22: Estimating the Image Center
Vanishing points:
  Due to perspective, all parallel lines in 3D space appear to meet in a point on the image - the vanishing point, which is the common intersection of all the image lines
Notes: A very important concept in perspective geometry for computer vision and computer graphics

## Slide 23: Estimating the Image Center
Vanishing points:
  Due to perspective, all parallel lines in 3D space appear to meet in a point on the image - the vanishing point, which is the common intersection of all the image lines
VP1
Notes: Images of a set of parallel lines generates a vanishing points

## Slide 24: Estimating the Image Center
Vanishing points:
  Due to perspective, all parallel lines in 3D space appear to meet in a point on the image - the vanishing point, which is the common intersection of all the image lines
Important property:
  Vector OV (from the center of projection to the vanishing point) is parallel to the parallel lines
O
VP1
Y
X
Z
Notes: Images of a set of parallel lines generates a vanishing points
Vector OV (from the center of projection to the vanishing point) is parallel to the parallel lines

## Slide 25: Estimating the Image Center
Vanishing points:
  Due to perspective, all parallel lines in 3D space appear to meet in a point on the image - the vanishing point, which is the common intersection of all the image lines
VP1
VP2
Notes: Differents sets have different vanishing points

## Slide 26: Estimating the Image Center
Orthocenter Theorem:
  Input: three mutually orthogonal sets of parallel lines in an image
  T: a triangle on the image plane defined by the three vanishing points
  Image center = orthocenter of triangle T
  Orthocenter of a triangle is the common intersection of the three altitudes
VP1
VP2
VP3
Notes: Three orthogonal sets of parallel lines can be used to determine the image center without any information about focal length and extrinsic parameters
Assumptions:
NO radial lens distortion
Questions:
Does the unknown aspect ration matter or not ??? YES

## Slide 27: Estimating the Image Center
Orthocenter Theorem:
  Input: three mutually orthogonal sets of parallel lines in an image
  T: a triangle on the image plane defined by the three vanishing points
  Image center = orthocenter of triangle T
  Orthocenter of a triangle is the common intersection of the three altitudes
VP1
VP2
VP3
Notes: This is not a good example since the VP3 is too far away from the image… Anyway just show the principle
Invalid case: one set of parallel lines is parallel to the image plane

## Slide 28: Estimating the Image Center
Orthocenter Theorem:
  Input: three mutually orthogonal sets of parallel lines in an image
  T: a triangle on the image plane defined by the three vanishing points
  Image center = orthocenter of triangle T
  Orthocenter of a triangle is the common intersection of the three altitudes
Orthocenter Theorem:
  WHY?
VP1
VP2
VP3
h3
h1
h2
(ox,oy)
Notes: Proof:
Define the center of projection of the camera is O (in 3D space).
L1, L2 and L3 are three mutually orthogonal sets of parallel lines
OVi points to the direction of the parallel set Li (i=1,2,3)
So Ovi is perpendicular to Ovj ( i=\= j) , therefore Ov3 is perpendicular to V1V2
ViHi is the altitude from Vi (I=1,2,3), therefore V3H3 is perpendicular to V1V2
Define the center of image is o, therefore Oo is perpendicular to the image plane
Therefore, o is the projection of O in the image plane, which lies on the altitude O3H3.
Similarly, o lies in O1H1 and O2H2, hence o is the intersection of H1, H2 and H3. #

## Slide 29: Estimating the Image Center
Assumptions:
  Known aspect ratio
  Without lens distortions
Questions:
  Can we solve both aspect ratio and the image center?
  How about with lens distortions?
VP1
VP2
VP3
h3
h1
h2
(ox,oy) ?
Notes: Questions:
Do we need to know the aspect ratio in advance?
  In the figure, we exaggerate the (wrong) aspect ration. The vanishing points are correct; but the image center will not at (ox, oy) since hi is not the altitude any more
How about an algorithm with radial distortion?

## Slide 30: Direct parameter Calibration Summary
Algorithm (p130-131)
  0. Estimate image center (and aspect ratio)
  Measure N 3D coordinates (Xi, Yi,Zi)
  Locate their corresponding image (xi,yi) - Edge, Corner, Hough
  Build matrix A of a homogeneous system Av = 0
  Compute SVD of A , solution v
  Determine aspect ratio a and scale |g|
  Recover the first two rows of R and the first two components of T up to a sign
  Determine sign s of g by checking the projection equation
  Compute the 3rd row of R by vector product, and enforce orthogonality constraint by SVD
  Solve Tz and fx using Least Square and SVD , then fy = fx / a
Yw
Xw
Zw
Notes: Two important steps:
Build a linear system
Decompose intrinsic and extrinsic parameters using physical constraints of the camera (orthogonality of R, sign of depth, ….)
SVD is used three times
homogeneous system
enforcing orthogonality constraints
solve least square system

## Slide 31: Remaining Issues and Possible Solution
Original assumptions:
  Without lens distortions
  Known aspect ratio when estimating image center
  Known image center when estimating others including aspect ratio
New Assumptions
  Without lens distortion
  Aspect ratio is approximately 1, or a = fx/fy = 4:3 ; image center about (M/2, N/2) given a MxN image
Solution (?)
  Using a = 1 to find image center (ox, oy)
  Using the estimated center to find others including a
  Refine image center using new a ; if change still significant, go to step 2; otherwise stop
  Projection Matrix Approach
Notes: Questions:
Do we need to know the aspect ratio in advance?
  In the figure, we exaggerate the (wrong) aspect ration. The vanishing points are correct; but the image center will not at (ox, oy) since hi is not the altitude any more
How about an algorithm with radial distortion?

## Slide 32: Linear Version of Perspective Projection
World to Camera
  Camera: P = (X,Y,Z)T
  World: Pw = (Xw,Yw,Zw)T
  Transform: R, T
Camera to Image
  Camera: P = (X,Y,Z)T
  Image: p = (x,y)T
  Not linear equations
Image to Frame
  Neglecting distortion
  Frame (xim, yim)T
World to Frame
  (Xw,Yw,Zw)T -> (xim, yim)T
  Effective focal lengths
    fx = f/sx, fy=f/sy
Notes: The 4th equation is derived from the three basic equations (pose, projection and frame), which directly maps a 3D world point to its frame coordinates

## Slide 33: Linear Matrix Equation of perspective projection
Projective Space
  Add fourth coordinate
    Pw = (Xw,Yw,Zw, 1)T
  Define (u,v,w)T such that
    u/w =xim, v/w =yim
3x4 Matrix Eext
  Only extrinsic parameters
  World to camera
3x3 Matrix Eint
  Only intrinsic parameters
  Camera to frame
Simple Matrix Product! Projective Matrix M= MintMext
  (Xw,Yw,Zw)T -> (xim, yim)T
  Linear Transform from projective space to projective plane
  M defined up to a scale factor – 11 independent entries
Notes: Show how the operations work in the blackboard

## Slide 34: Projection Matrix M
World – Frame Transform
  Drop “im” and “w”
  N pairs (xi,yi) <-> (Xi,Yi,Zi)
  Linear equations of m
3x4 Projection Matrix M
  Both intrinsic (4) and extrinsic (6) – 10 parameters
Notes: Show how the operations work in the blackboard

## Slide 35: Step 1: Estimation of projection matrix
World – Frame Transform
  Drop “im” and “w”
  N pairs (xi,yi) <-> (Xi,Yi,Zi)
Linear equations of m
  2N equations, 11 independent variables
  N >=6 , SVD => m up to a unknown scale
Notes: Show how the operations work in the blackboard

## Slide 36: Step 2: Computing camera parameters
3x4 Projection Matrix M
  Both intrinsic and extrinsic
From M^ to parameters
  Find scale |g| by using unit vector R3T
  Determine Tz and sign of g from m34 (i.e. q43)
  Obtain R3T
  Find (ox, oy) by dot products of Rows q1. q3, q2.q3, using the orthogonal constraints of R
  Determine fx and fy from q1 and q2
  All the rest: R1T, R2T, Tx, Ty
  Enforce orthognoality on R?
Notes: Show how the operations work in the blackboard

## Slide 37: Comparisons
Direct parameter method and Projection Matrix method
Properties in Common:
  Linear system first, Parameter decomposition second
  Results should be exactly the same
Differences
  Number of variables in homogeneous systems
    Matrix method: All parameters at once, 2N Equations of 12 variables
    Direct method in three steps: N Equations of 8 variables, N equations of 2 Variables, Image Center – maybe more stable
  Assumptions
    Matrix method: simpler, and more general; sometime projection matrix is sufficient so no need for parameter decomposition
    Direct method: Assume known image center in the first two steps, and known aspect ratio in estimating image center
Notes: Direct parameter method: One point pair will provide 1 linear equation of 8 unknowns (7 independent)
Projection matrix method: One point pair will provide 2 linear equations of 12 = (4+4+4) unknowns (11 independent)
All in one method (including image center): One point pair will provide 2 equations of 14 (4+4+4+2) unknowns, 2 linear equations of 20 (4+4+4+4+4) unknowns

## Slide 38: Guidelines for Calibration
Pick up a well-known technique or a few
Design and construct calibration patterns (with known 3D)
Make sure what parameters you want to find for your camera
Run algorithms on ideal simulated data
  You can either use the data of the real calibration pattern or using computer generated data
  Define a virtual camera with known intrinsic and extrinsic parameters
  Generate 2D points from the 3D data using the virtual camera
  Run algorithms on the 2D-3D data set
Add noises in the simulated data to test the robustness
Run algorithms on the real data (images of calibration target)
If successful, you are all set
Otherwise:
  Check how you select the distribution of control points
  Check the accuracy in 3D and 2D localization
  Check the robustness of your algorithms again
  Develop your own algorithms  NEW METHODS?
Notes: Direct parameter method: One point pair will provide 1 linear equation of 8 unknowns (7 independent)
Projection matrix method: One point pair will provide 2 linear equations of 12 = (4+4+4) unknowns (11 independent)
All in one method (including image center): One point pair will provide 2 equations of 14 (4+4+4+2) unknowns, 2 linear equations of 20 (4+4+4+4+4) unknowns

## Slide 39: Next
3D reconstruction using two cameras
Stereo Vision
& project discussions
Homework #2