## Slide 1: 3D Vision
Topic 1 of Part II
Camera Models
Computer Vision
Zhigang Zhu, City College of New York zzhu@ccny.cuny.edu
Notes: This course is a basic introduction to parts of the field of computer vision. This version of the course covers topics in 'early' or 'low' level vision and parts of 'intermediate' level vision. It assumes no background in computer vision, a minimal background in Artificial Intelligence and only basic concepts in calculus, linear algebra, and probability theory.

## Slide 2: 3D Vision
Closely Related Disciplines
  Image Processing – images to mages
  Computer Graphics – models to images
  Computer Vision – images to models
  Photogrammetry – obtaining accurate measurements from images
What is 3-D ( three dimensional) Vision?
  Motivation: making computers see (the 3D world as humans do)
  Computer Vision: 2D images to 3D structure
  Applications : robotics / VR /Image-based rendering/ 3D video
Lectures on 3-D Vision Fundamentals
  Camera Geometric Models (1 lecture)
  Camera Calibration (1 lecture)
  Stereo (2 lectures)
  Motion (2 lectures)

## Slide 3: Lecture Outline
Geometric Projection of a Camera
  Pinhole camera model
  Perspective projection
  Weak-Perspective Projection
Camera Parameters
  Intrinsic Parameters: define mapping from 3D to 2D
  Extrinsic parameters: define viewpoint and viewing direction
    Basic Vector and Matrix Operations, Rotation
Camera Models Revisited
  Linear Version of the Projection Transformation Equation
    Perspective Camera Model
    Weak-Perspective Camera Model
    Affine Camera Model
    Camera Model for Planes
Summary

## Slide 4: Lecture Assumptions
Camera Geometric Models
  Knowledge about 2D and 3D geometric transformations
  Linear algebra (vector, matrix)
  This lecture is only about geometry
Goal
Build up relation between 2D images and 3D scenes
3D Graphics (rendering): from 3D to 2D
3D Vision (stereo and motion): from 2D to 3D
  Calibration: Determning the parameters for mapping
Notes: Our goal is to build the geometric relations between a 3D scene and its 2D images for both computer vision and computer graphics. The relations include two aspects: 3D transformation that represents the viewpoints and viewing directions of the camera (real or virtual), and the perspective projection maps 3D points into 2D images.
Note that we can use the same sets of equations for both vision and graphics. However vision is much harder than graphics: In graphics, 2D projections can be easily generated from 3D models, given the 3D models and the (virtual) camera parameters. In computer vision, the projections are fulfilled by a real camera. We want to reconstruct the 3D models from the 2D images. The inverse problems are much harder since (1) we need to find out the intrinsic and extrinsic camera parameters by the so called calibration procedure; and (2) we need to recover 3D from 2D images in which the third dimension is lost.

## Slide 5: Image Formation
Notes: Let's start with an overview of the process up to the creation of the signal. For the sake of the example, we assume that the light source is the sun, the surface represents a small portion of the surface of an object, and the optical system is composed of a simple pinhole lens. Light from the sun is incident on the surface, which in turn reflects some of the incident light. Part of the light reflected from the surface is captured by the pinhole lens and is projected onto the imaging plane.
The point on the imaging plane represented by the dot corresponds to the image location of the corresponding point on the surface. Clearly a different point on the imaging plane would correspond to a different point on the surface.
If the imaging plane is a piece of black and white film, as in a real camera, the representation of the intensity of the light reflecting from the surface is recorded by the silver density in the negative. The more light reflected from the surface, the denser the silver grains in the film become. When the negative is then printed, the corresponding location is bright, since the dense silver grains reduce the amount of light reaching the photographic paper surface.
In the case of color film, three separate silver emulsions are used. Each emulsion is selectively sensitive to light of different frequencies: red, green, and blue. From these three color components, the full spectrum of color available in the original scene can be reconstructed. Note that this is not strictly true; there are colors which cannot be reconstructed in this way due to limitations in the color dyes available. When the three emulsions are printed on color sensitive paper containing three layers, we get the familiar color print.
In the case of a black and white TV camera, the intensity of the light is coded in the amplitude of the electrical signal produced by the camera. For color TV cameras, the signal contains values for the red, green, and blue components of the incident light at a point.

## Slide 6: Image Formation
L
i
g
h
t
(
E
n
e
r
g
y
)
S
o
u
r
c
e
S
u
r
f
a
c
e
P
i
n
h
o
l
e
L
e
n
s
I
m
a
g
i
n
g
P
l
a
n
e
W
o
r
l
d
O
p
t
i
c
s
S
e
n
s
o
r
S
i
g
n
a
l
Camera: Spec & Pose
3D Scene
2D Image
Notes: In the geometric point of view, the camera is a device that convert 3D scenes into 2D images. As we usually do in the real life, the locations and orientations of the camera change in order to capture good views of the scenes. In computer vision, in order to recover the 3D structure of the scenes from their 2D images, we need to build the relations between the 2D images and the 3D scenes, through the camera. The parameters of the camera include two parts: the intrinsic parameters that map the 3D points into 2D images, and the extrinsic parameters that represent the position and orientation (POSE) of the camera

## Slide 7: Pinhole Camera Model
Pin-hole is the basis for most graphics and vision
  Derived from physical construction of early cameras
  Mathematics is very straightforward
3D World projected to 2D Image
  Image inverted, size reduced
  Image is a 2D plane: No direct depth information
Perspective projection
  f called the focal length of the lens
  given image size, change f will change FOV and figure sizes
Notes: First, Let’s have a look at the camera model- without consider the pose of the camera.
In the diagram, f is called the focal length of the (pinhole) lens and is the distance from the center of the lens to the image plane measured along the optical axis. The center of the lens (center of projection) is the point in the lens system through which all rays must pass.
From the diagram, it is easy to see that the image projected onto the image plane is inverted. The ray from the cartoon figure's head, for example, is projected to a point near the bottom of the image plane, while the ray from a point on the figure's foot is projected to a point near the top of the image plane.
Various coordinate reference frames can be associated with the pinhole camera system. In most of them, the Z axis coincides with the optical axis (also called the central projection ray). By convention, the image plane is located at Z = -f and the lens is located at Z = 0. Z is also the distance to an object as measured along the optical axis; also by convention, Z is positive coming out of the camera. The X and Y axis lie in the image place - we will establish exactly how later.
It is possible to reverse the position of the image plane and the camera lens so that the projected image is upright....

## Slide 8: Focal Length, FOV
Consider case with object on the optical axis:
Optical axis: the direction of imaging
Image plane: a plane perpendicular to the optical axis
Center of Projection (pinhole), focal point, viewpoint, nodal point
Focal length: distance from focal point to the image plane
FOV : Field of View – viewing angles in horizontal and vertical directions
f
z
viewpoint
Image plane
Notes: Several important terms for perspective projections
Basic properties: Figure sizes and FOV versus focal length
Image resolutions

## Slide 9: Focal Length, FOV
Consider case with object on the optical axis:
f
z
Out of view
Image plane
Optical axis: the direction of imaging
Image plane: a plane perpendicular to the optical axis
Center of Projection (pinhole), focal point, viewpoint, , nodal point
Focal length: distance from focal point to the image plane
FOV : Field of View – viewing angles in horizontal and vertical directions
Increasing f will enlarge figures, but decrease FOV
Notes: Simple geometry of the pinhole camera

## Slide 10: Equivalent Geometry
Consider case with object on the optical axis:
f
z
More convenient with upright image:
f
z
Projection plane z = f
Equivalent mathematically
Notes: These geometries are equivalent mathematically. In the second case, the center of projection is still located at 0 along the optical axis. However, the image plane is placed at z=f.
The equivalence of both geometries can be established by recognizing that the two triangles in the upper diagram are similar to the two triangles in the lower diagram. In fact, it is exactly this relationship which will allow us to derive the perspective projection equations.....

## Slide 11: Perspective Projection
Compute the image coordinates of p in terms of the world (camera) coordinates of P.
Origin of camera at center of projection
Z axis along optical axis
Image Plane at Z = f; x // X and y//Y
x
y
Z
P(
X,Y,Z
)
p(x, y)
Z = f
0
Y
X
Notes: Our goal is to compute the image coordinates of the point P located at (X,Y,Z) in the world coordinate system under perspective projection. Equivalently, we want to know where the ray passing through the point P and the center of the camera lens located at the center of projection (0) pierces the image plane. We can do this rather simply by examining the projections of the point P on the (X,Z) and (Y,Z) planes.
Here we are assuming the camera coordinate system coincides with the world.

## Slide 12: Reverse Projection
Given a center of projection and image coordinates of a point, it is not possible to recover the 3D depth of the point from a single image.
In general, at least two images of the same point taken from two different locations are required to recover depth.
Notes: We have seen that, given the coordinates of a point (X,Y,Z) and the focal length of the lens f, the image coordinates (x,y) of the projection of the point on the image plane can be uniquely computed. Now let us ask the reverse question: Given the coordinates (x,y) of a point in the image, can we uniquely compute the world coordinates (X,Y,Z) of the point? In particular, can we recover the depth of the point (Z)?
To see that this is not possible, consider the infinitely extended ray through the center of projection and the point (x,y) on the image plane. Any point P in the world coordinate system which lies along this ray will project to the same image coordinates. Thus, in the absence of any additional information about P, we cannot determine its world coordinates from knowledge of the coordinates of its image projection.
However, it is easy to show that if we know the image coordinates of the point P in two images taken from different world coordinate locations, and if we know the relationship between the two sensor locations, then 3D information about the point can be recovered. This is known as stereo vision; in the human visual system, our two eyes produce slightly different images of the scene and from this we experience a sensation of depth.

## Slide 13: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam : what do you see in this picture?
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: We may see
Objects : river, river bank, cars parking on the bank, buildings, tree in front of the buildings, bridge, sky.
Can figure out relative distances – SO WHAT? Do we see the 3D structure with just one images?
Let’s first have a look at what geometric properties are preserved in the 2D perspective image.

## Slide 14: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: Straightness is preserved
Proof. x= fX/Z, y=fY/Z: a 3D line in space projects to a 2D line in the image

## Slide 15: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: Size is inversely proportional to the depth (distance) Z

## Slide 16: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: In general, the angles and parallelism are not preserved. For example, the right angles of the rectangular building change: Acute angles (smaller than 90) in the nearer end and obtuse angles (greater than 90) in the farther end….

## Slide 17: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: The projections of parallel lines converge to a point. --- vanishing point
So the shapes usually change
How about planes parallel to the image plane… we may not be able to find such a plane in this image, but…

## Slide 18: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  parallel to image
  depth
Notes: The façade of building in the far end approximately is parallel to the image plane so the shape is preserved

## Slide 19: Pinhole camera image
- We see spatial shapes rather than individual pixels
- Knowledge: top-down vision belongs to human
- Stereo &Motion most successful in 3D CV & applications
- You can see it but you don't know how…
Amsterdam: what do you see?
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  parallel to image
  Depth ?
    stereo
    motion
    size
    structure …
Notes: SO why can we see 3D structure from a single image?
We do not see individual pixels, but rather spatial shapes
We use knowledge of the objects (RECTANGULAR building, similar size of the cars), river and bank in a plane – perceptual organization (up-down vision)
Perspective distortion actually tells us some 3D information: Using the projections of parallel lines in the façade of the building, we can estimate the orientation of the building therefore 3D structure
Order of the object, Occlusion,
BUT it is extremely hard for a computer to use high level knowledge . Up-down paradigm seems to be the privilege of human visual perception. The state-of-the-art of the computer vision mainly use bottom-up approach. SO
Stereo
Motion
The idea is to recover 3D of each small local pieces (point, line, patch), and then group and segment the 3D point cloud into meaningful objects so that the computer may recognize the objects in images
Intermediate results for image and video representations, coding and compression, interactive 3D presentation and event detection
image mosaics for entertainment, interface, virtual reality, and monitoring
Layered representation (MPEG4)
3D video
Motion Detection (of human, cars) for surveillance, traffic monitoring,
Human Vision: You can see it but you don't know how you see it.

## Slide 20: Yet other pinhole camera images
Markus Raetz, Metamorphose II, 1991-92, cast iron, 15 1/4 x 12 x 12 inches
Fine Art Center University Gallery, Sep 15 – Oct 26
Rabbit or Man?
Notes: What do you see? What are their relation?

## Slide 21: Yet other pinhole camera images
Markus Raetz, Metamorphose II, 1991-92, cast iron, 15 1/4 x 12 x 12 inches
Fine Art Center University Gallery, Sep 15 – Oct 26
2D projections are not the “same” as the real object as we usually see everyday!
Notes: All of them are 2D projections of the same 3D real object!
Vision is a complicated thing!
What you see is not what it is.

## Slide 22: It’s real!

## Slide 23: Weak Perspective Projection
Average depth Z is much larger than the relative distance between any two scene points measured along the optical axis
A sequence of two transformations
  Orthographic projection : parallel rays
  Isotropic scaling : f/Z
Linear Model
  Preserve angles and shapes
x
y
Z
P(
X,Y,Z
)
p(x, y)
Z = f
0
Y
X
Notes: The relative range of an object is much smaller than the distance from the camera to the object
All the points in the object have the same Z so its image is just a scaled version of the real object
Equivalently, the projection can be viewed as an orthogonal projection with parallel rays from the object to the image plane, followed by a isotropic scaling.

## Slide 24: Camera Parameters
Coordinate Systems
  Frame coordinates (xim, yim) pixels
  Image coordinates (x,y) in mm
  Camera coordinates (X,Y,Z)
  World coordinates (Xw,Yw,Zw)
Camera Parameters
  Intrinsic Parameters (of the camera and the frame grabber): link the frame coordinates of an image point with its corresponding camera coordinates
  Extrinsic parameters: define the location and orientation of the camera coordinate system with respect to the world coordinate system
Zw
Xw
Yw
Y
X
Z
x
y
O
Pw
P
p
xim
yim
(xim,yim)
Pose / Camera
Object / World
Image frame
Frame Grabber
Notes: The entire story of the camera model: from world to camera (coordinate systems), and from camera (3D) to image frame (2D).
The intrinsic parameters should be listed in the specifications of the camera and the frame grabber by the manufacturers, but not really….
The extrinsic parameters describe the pose (position and orientation) of the camera looking at the scene.

## Slide 25: Intrinsic Parameters (I)
From image to frame
  Image center
  Directions of axes
  Pixel size
From 3D to 2D
  Perspective projection
Intrinsic Parameters
  (ox ,oy) : image center (in pixels)
  (sx ,sy) : effective size of the pixel (in mm)
  f: focal length
xim
yim
Pixel
(xim,yim)
Y
Z
X
x
y
O
p (x,y,f)
ox
oy
(0,0)
Size:
(sx,sy)

## Slide 26: Intrinsic Parameters (II)
Lens Distortions
Modeled as simple radial distortions
  r2 = xd2+yd2
  (xd , yd) distorted points
  k1 , k2: distortion coefficients
  A model with k2 =0 is still accurate for a CCD sensor of 500x500 with ~5 pixels distortion on the outer boundary
(xd, yd)
(x, y)
k1 , k2
Notes: In some real applications, such as accurate 3D measurement and really distorted lens (wide angle lens for example), you really need to consider to remove the distortion. For the purpose of showing you the principle of 3D geometry and calibration let’s forget about the radial distortion for the moment.

## Slide 27: Extrinsic Parameters
From World to Camera
Extrinsic Parameters
  A 3-D translation vector, T, describing the relative locations of the origins of the two coordinate systems (what’s it?)
  A 3x3 rotation matrix, R, an orthogonal matrix that brings the corresponding axes of the two systems onto each other
Zw
Xw
Yw
Y
X
Z
x
y
O
Pw
P
p
xim
yim
(xim,yim)
T
Notes: This equation is very important, so are the rotation matrix and the translation vector. We are going to discuss more in the next few slides…
Basic linear algebra
the physical meanings of them

## Slide 28: Linear Algebra: Vector and Matrix
A point as a 2D/ 3D vector
  Image point: 2D vector
  Scene point: 3D vector
  Translation: 3D vector
Vector Operations
  Addition:
    Translation of a 3D vector
  Dot product ( a scalar):
    a.b = |a||b|cosq
  Cross product (a vector)
    Generates a new vector that is orthogonal to both of them
T: Transpose
a x b = (a2b3 - a3b2)i + (a3b1 - a1b3)j + (a1b2 - a2b1)k
Notes: Show how the Vector operations work in the blackboard
Dot product: a.b = |a||b|cosq
magnitude of the projection of a vector on the other;
angle between the two vector.
0 when they are orthogonal
Vector (cross) product
Generates a new vector that is orthogonal to both of them
a x b = (a2b3 - a3b2)i + (a3b1 - a1b3)j + (a1b2 - a2b1)k
| i j k |
| a1 a2 a3|
| b1 b2 b3|

## Slide 29: Linear Algebra: Vector and Matrix
Rotation: 3x3 matrix
  Orthogonal :
    9 elements => 3+3 constraints (orthogonal/cross ) => 2+2 constraints (unit vectors) => 3 DOF ? (degrees of freedom, orthogonal/dot)
  How to generate R from three angles? (next few slides)
Matrix Operations
  R Pw +T= ? - Points in the World are projected on three new axes (of the camera system) and translated to a new origin
Notes: Rotation Matrix
Orthogonal
R3 = R1 X R2
R1’, R2’ and R3’ are the three camera axes (X, Y, Z) in the world coordinate system

## Slide 30: Camera Parameters
Coordinate Systems
  Frame coordinates (xim, yim) pixels
  Image coordinates (x,y) in mm
  Camera coordinates (X,Y,Z)
  World coordinates (Xw,Yw,Zw)
Camera Parameters
  Intrinsic Parameters (of the camera and the frame grabber): link the frame coordinates of an image point with its corresponding camera coordinates
  Extrinsic parameters: define the location and orientation of the camera coordinate system with respect to the world coordinate system
Zw
Xw
Yw
Y
X
Z
x
y
O
Pw
P
p
xim
yim
(xim,yim)
Pose / Camera
Object / World
Image frame
Frame Grabber
Notes: The entire story of the camera model: from world to camera (coordinate systems), and from camera (3D) to image frame (2D).
The intrinsic parameters should be listed in the specifications of the camera and the frame grabber by the manufacturers, but not really….
The extrinsic parameters describe the pose (position and orientation) of the camera looking at the scene.

## Slide 31: Rotation: from Angles to Matrix
Rotation around the Axes
  Result of three consecutive rotations around the coordinate axes
Notes:
  Only three rotations
  Every time around one axis
  Bring corresponding axes to each other
    Xw = X, Yw = Y, Zw = Z
  First step (e.g.) Bring Xw to X
Zw
Xw
Yw
Y
X
Z
O
g
b
a
Notes: Constructing a rotation matrix from three independent rotation angles is not at all a trivial thing. Let’s first move origin of the camera coordinate system to that of the world. Then the goal is to bring three axes of the world coordinate system to the corresponding axes of the camera coordinate system. The result will give us the transformation of the coordinates of a point from the world coordinate system to the camera coordinate system. Attention should be paid to the directions of the rotations (that sign of the sine term) to make sure that we have the correct transformation.
The constraints of the rotations are that every time we can only rotate around one of the axes of the (changing) world coordinate system. Let’s assume we will rotate in the order of g,b,a around Zw, Yw and Zw consecutively. As a first step, we try to bring one of the axes, e.g. Xw to its corresponding axis (e.g. X) in the camera coordinate system. However it cannot be achieved by a single rotation around Zw axes since X usually is not in the plane XwOYw. We need to achieve this goal in two steps. First, we rotate the world coordinate system around Zw axis until Yw is perpendicular to X. Due to the orthogonal coordinate systems of XwYwZw and XYZ, X (OX) must be in the plane XwOZw (and consequently Yw in the plane YOZ since X can only be perpendicular to a line in the plane YOZ that passes through O) . So next time we can bring Xw to X by rotating the world coordinate system around the new Yw axis since X is in the plane XwOZw. After this rotation, both Yw and Zw will be in the plane XOZ so that a rotation around the new Xw (i.e. X) will bring Yw to Y and Zw to Z simultaneously.

## Slide 32: Rotation: from Angles to Matrix
Rotation g around the Zw Axis
  Rotate in XwOYw plane
  Goal: Bring Xw to X
  But X is not in XwOYw
  YwX X in XwOZw (Yw XwOZw)  Yw in YOZ ( X YOZ)
Next time rotation around Yw
Zw
Xw
Yw
Y
X
Z
O
g
Notes: Goal:
Rotate until Yw is perpendicular to X, so that X will be in the plane XwOZw. Next time we can bring Xw to X by rotating around the Yw axis.
By-product:
New Yw will be in the plane YOZ.

## Slide 33: Rotation: from Angles to Matrix
Rotation g around the Zw Axis
  Rotate in XwOYw plane so that
  YwX X in XwOZw (YwXwOZw)  Yw in YOZ (  XYOZ)
Zw does not change
Zw
Xw
Yw
Y
X
Z
O
g
Notes: explain what the rotation matrix look like:
just like a 2D rotation in the plane XwOYw
Note the sign in front of the sine term
Results:
X in the plane XwOZw
Yw in the plane YOZ

## Slide 34: Rotation: from Angles to Matrix
Rotation b around the Yw Axis
  Rotate in XwOZw plane so that
  Xw = X  Zw in YOZ (& Yw in YOZ)
Yw does not change
Zw
Xw
Yw
Y
X
Z
O
b
Notes: Goal:
Bring Xw to X
By-product:
Zw in YOZ

## Slide 35: Rotation: from Angles to Matrix
Rotation b around the Yw Axis
  Rotate in XwOZw plane so that
  Xw = X  Zw in YOZ (& Yw in YOZ)
Yw does not change
Zw
Xw
Yw
Y
X
Z
O
b
Notes: Results
Xw = X
Zw in YOZ

## Slide 36: Rotation: from Angles to Matrix
Rotation a around the Xw(X) Axis
  Rotate in YwOZw plane so that
  Yw = Y, Zw = Z (& Xw = X)
Xw does not change
Zw
Xw
Yw
Y
X
Z
O
a
Notes: Goal:
Bring Yw to Y, Zw to Z

## Slide 37: Rotation: from Angles to Matrix
Rotation a around the Xw(X) Axis
  Rotate in YwOZw plane so that
  Yw = Y, Zw = Z (& Xw = X)
Xw does not change
Zw
Xw
Yw
Y
X
Z
O
a
Notes: Done

## Slide 38: Rotation: from Angles to Matrix
Rotation around the Axes
  Result of three consecutive rotations around the coordinate axes
Notes:
  Rotation directions
  The order of multiplications matters: g,b,a
  Same R, 6 different sets of a,b,g
  R Non-linear function of a,b,g
  R is orthogonal
  It’s easy to compute angles from R
Zw
Xw
Yw
Y
X
Z
O
g
b
a
Appendix A.9 of the textbook
Notes: 3! Different sets of rotation angles
Factorial of 3 = 3x2x1=6

## Slide 39: Rotation- Axis and Angle
According to Euler’s Theorem, any 3D rotation can be described by a rotating angle, q, around an axis defined by an unit vector n = [n1, n2, n3]T.
Three degrees of freedom – why?
The third way to look at the rotation
Notes: I is the identity matrix, {1 0 0; 0 1 0; 0 0 1} 3x3
Eu·ler Pronunciation: 'oi-l&r Function: biographical name Leonhard 1707-1783 Swiss mathematician & physicist; made contributions in geometry, calculus, number theory; developed problem-solving methods in astronomy, applications of mathematics in technology

## Slide 40: Linear Version of Perspective Projection
World to Camera
  Camera: P = (X,Y,Z)T
  World: Pw = (Xw,Yw,Zw)T
  Transform: R, T
Camera to Image
  Camera: P = (X,Y,Z)T
  Image: p = (x,y)T
  Not linear equations
Image to Frame
  Neglecting distortion
  Frame (xim, yim)T
World to Frame
  (Xw,Yw,Zw)T -> (xim, yim)T
  Effective focal lengths
    fx = f/sx, fy=f/sy
    Three are not independent
Notes: Show how the operations work in the blackboard

## Slide 41: Linear Matrix Equation of perspective projection
Projective Space
  Add fourth coordinate
    Pw = (Xw,Yw,Zw, 1)T
  Define (x1,x2,x3)T such that
    x1/x3 =xim, x2/x3 =yim
3x4 Matrix Mext
  Only extrinsic parameters
  World to camera
3x3 Matrix Mint
  Only intrinsic parameters
  Camera to frame
Simple Matrix Product! Projective Matrix M= MintMext
  (Xw,Yw,Zw)T -> (xim, yim)T
  Linear Transform from projective space to projective plane
  M defined up to a scale factor – 11 independent entries
Notes: Show how the operations work in the blackboard

## Slide 42: Three Camera Models
Perspective Camera Model
  Making some assumptions
    Known center: Ox = Oy = 0
    Square pixel: Sx = Sy = 1
  11 independent entries <-> 7 parameters
Weak-Perspective Camera Model
  Average Distance Z >> Range dZ
  Define centroid vector Pw
  8 independent entries
Affine Camera Model
  Mathematical Generalization of Weak-Pers
  Doesn’t correspond to physical camera
  But simple equation and appealing geometry
    Doesn’t preserve angle BUT parallelism
  8 independent entries
Notes: Show how the operations work in the blackboard
Perspective : 3x4 - 1 independent parameters in M
Weak perspective 2x4+1-1
affine 8

## Slide 43: Camera Models for a Plane
Planes are very common in the Man-Made World
  One more constraint for all points: Zw is a function of Xw and Yw
Special case: Ground Plane
  Zw=0
  Pw =(Xw, Yw,0, 1)T
  3D point -> 2D point
Projective Model of a Plane
  8 independent entries
General Form ?
  8 independent entries
Notes: Show how the operations work in the blackboard

## Slide 44: Camera Models for a Plane
A Plane in the World
  One more constraint for all points: Zw is a function of Xw and Yw
Special case: Ground Plane
  Zw=0
  Pw =(Xw, Yw,0, 1)T
  3D point -> 2D point
Projective Model of Zw=0
  8 independent entries
General Form ?
  8 independent entries
Notes: Show how the operations work in the blackboard

## Slide 45: Camera Models for a Plane
A Plane in the World
  One more constraint for all points: Zw is a function of Xw and Yw
Special case: Ground Plane
  Zw=0
  Pw =(Xw, Yw,0, 1)T
  3D point -> 2D point
Projective Model of Zw=0
  8 independent entries
General Form ?
  nz = 1
  8 independent entries
2D (xim,yim) -> 3D (Xw, Yw, Zw) ?
Notes: Show how the operations work in the blackboard

## Slide 46: Applications and Issues
Graphics /Rendering
  From 3D world to 2D image
    Changing viewpoints and directions
    Changing focal length
  Fast rendering algorithms
Vision / Reconstruction
  From 2D image to 3D model
    Inverse problem
    Much harder / unsolved
  Robust algorithms for matching and parameter estimation
  Need to estimate camera parameters first
Calibration
  Find intrinsic & extrinsic parameters
  Given image-world point pairs
  Probably a partially solved problem ?
  11 independent entries
    <-> 10 parameters: fx, fy, ox, oy, a,b,g, Tx,Ty,Tz
Notes: Show how the operations work in the blackboard

## Slide 47: Camera Model Summary
Geometric Projection of a Camera
  Pinhole camera model
  Perspective projection
  Weak-Perspective Projection
Camera Parameters (10 or 11)
  Intrinsic Parameters: f, ox,oy, sx,sy,k1: 4 or 5 independent parameters
  Extrinsic parameters: R, T – 6 DOF (degrees of freedom)
Linear Equations of Camera Models (without distortion)
  General Projection Transformation Equation : 11 parameters
  Perspective Camera Model: 11 parameters
  Weak-Perspective Camera Model: 8 parameters
  Affine Camera Model: generalization of weak-perspective: 8
  Projective transformation of planes: 8 parameters

## Slide 48: Next
Determining the value of the extrinsic and intrinsic parameters of a camera
Calibration